## Slide 1: Energy Year 2024 District Heating
28.01.2025
Finnish Energy
District heating preliminary data 2024

## Slide 2: Share of climate neutral energy continued to grow Share of renewables, heat recovery and electric boilers increased from 70 percent to 73 percent
Heat recovery (also renewable heat produced with heat pumps): otherwise unutilised heat energy, e.g. heat recovery from wastewater, flue gases, return water from district cooling.
Waste: municipal waste, recovered fuels, demolition wood, impregnated wood, plastic waste and hazardous waste.
Other biofuels: wood pellets, recovered wood, black liquor tai other biomass
Others: steam, hydrogen.
2024
2023
Chart: 
| Forest fuelwood | Industrial wood residues | Other biofuels | Waste | Heat recovery | Electric boilers | Peat | Natural gas | Coal | Oil | Others
 | 0.3 | 0.12 | 0.06 | 0.1 | 0.16 | 0.04 | 0.06 | 0.07 | 0.06 | 0.03 | 0

## Slide 3: District heating goes electric
Chart: GWh
| 2021 | 2022 | 2023 | 2024
Sähkökattiloiden tuottama lämpö | 16.0002 | 57.8799 | 745.639 | 1538.4784
Electric boilers produced 1540 GWh heat in 2024
Electric boilers reduce the use of fuels when electricity price is low
Heat generated by electric boilers

## Slide 4: Temperature corrected heat consumption stayed in the same level with the previous year
District heat consumption 31,8 TWh
  The heating season was 0,9 oC warmer than the normal year
Temperature corrected district heat consumption 33,5 TWh
  Temperature correction takes into account annual temperature differences.
Chart: TWh
| 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Measured consumption (TWh) | 4.6 | 5.2 | 5.9 | 7 | 6.5648 | 7.6852 | 9.847 | 10.2175 | 11.8359 | 12.1964 | 13.3044 | 14.2522 | 15.1359 | 16.1844 | 17.4651 | 21.6512 | 20.9948 | 23.6066 | 22.2379 | 20.8521 | 22.2664 | 23.4924 | 23.5859 | 24.645 | 25.3383 | 24.8457 | 26.668 | 26.3584 | 27.5136 | 26.9206 | 25.6435 | 28.3739 | 29.6107 | 30.5455 | 29.503 | 29.281 | 30.1203 | 30.1013 | 29.3175 | 32.4156 | 35.8949 | 31.1924 | 34.0488 | 31.7097 | 31.5571 | 30.0431 | 33.2247 | 33.1362 | 33.4532 | 33.1868 | 30.0973 | 35.2998 | 32.9769 | 33.2274 | 31.8354
Temperature corrected consumption (TWh) | 4.8241 | 5.2505 | 6.1164 | 6.6982 | 7.3966 | 8.1497 | 9.1701 | 10.1561 | 11.0678 | 12.0751 | 13.0346 | 14.1161 | 15.3377 | 16.6972 | 18.2961 | 19.6959 | 20.9513 | 21.8703 | 22.4792 | 23.0422 | 23.5306 | 24.2218 | 24.7101 | 25.1501 | 25.4695 | 25.6918 | 25.8783 | 26.5251 | 27.1391 | 28.1221 | 28.486 | 29.0216 | 29.5967 | 29.975 | 30.2775 | 30.2997 | 30.8559 | 31.3568 | 31.7177 | 31.875 | 32.2095 | 32.4864 | 32.7817 | 32.8458 | 33.1772 | 33.5263 | 33.7676 | 33.8883 | 34.0991 | 34.3159 | 34.3388 | 34.0677 | 33.9234 | 33.515 | 33.4833

## Slide 5: Monthly district heat demand
Year 2024 was 1 oC warmer than the normal period of 1991-2020
January and April were colder than normal, and the other months were warmer than normal.
The cold winter months exemplify the need for a wide palette of fuels to ensure the security of supply of heating.
Notes: Graafi päivitetty – data pitää vielä tarkistaa, vuoden 2022 alussa. (MT)

## Slide 6: District heating supports the Finnish electricity system

## Slide 7: Peak consumptions of district heat and electricity are close to each other
Chart: MW
Source: estimation is based on Entso-E and Helen open data 2024*, hourly demand, district heat demand scaled based on Helen's hourly data,
* Preliminary data for 2024.
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Hourly consumption of district heat and electricity in 2024
Despite a significant difference in overall demand for electricity and heat, peak consumptions are relatively close to each

## Slide 8: The energy transition in district heat production has advanced well

## Slide 9: Share of renewables has more than doubled and share of heat recovery has multiplied compared to year 2010 Share of renewables has increased from 18 to 48 percent and heat recovery from 2 to 16 percent
2024
2010
Chart: 
| Forest fuelwood | Industrial wood residues | Other biofuels | Waste | Heat recovery | Electric boilers | Peat | Natural gas | Coal | Oil | Others
 | 0.3 | 0.12 | 0.06 | 0.1 | 0.16 | 0.04 | 0.06 | 0.07 | 0.06 | 0.03 | 0
Chart: 
| Forest fuelwood | Industrial wood residues | Other biofuels | Waste | Heat recovery | Electric boilers | Peat | Natural gas | Coal | Oil | Others
 | 0.1 | 0.07 | 0.01 | 0.02 | 0.02 | 0 | 0.19 | 0.3 | 0.21 | 0.07 | 0.01

## Slide 10: Share of renewables and recovered heat is over 70 % in 2024
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
hiili | 0.436 | 0.451 | 0.41 | 0.412 | 0.402 | 0.375 | 0.3763 | 0.3611 | 0.2946 | 0.2782 | 0.2644 | 0.27427 | 0.26223 | 0.26059 | 0.25055 | 0.236 | 0.25409 | 0.23995 | 0.21754 | 0.22213 | 0.20477 | 0.22702 | 0.22332 | 0.24115 | 0.22424 | 0.19569 | 0.22914 | 0.22892 | 0.1944 | 0.17641 | 0.11486 | 0.11481 | 0.15235 | 0.080049 | 0.058533
öljy | 0.11 | 0.104 | 0.102 | 0.094 | 0.1 | 0.087 | 0.0824 | 0.0602 | 0.0709 | 0.0785 | 0.0841 | 0.091413 | 0.083644 | 0.080872 | 0.06411 | 0.057348 | 0.063641 | 0.065904 | 0.048745 | 0.072848 | 0.071663 | 0.046647 | 0.050259 | 0.0295 | 0.02814 | 0.029404 | 0.030642 | 0.021658 | 0.022122 | 0.019301 | 0.012498 | 0.029796 | 0.056688 | 0.027202 | 0.025532
maakaasu | 0.211 | 0.203 | 0.24 | 0.252 | 0.248 | 0.263 | 0.2594 | 0.2898 | 0.3424 | 0.3565 | 0.34489 | 0.31005 | 0.31767 | 0.30738 | 0.32993 | 0.33756 | 0.29743 | 0.29432 | 0.31545 | 0.28982 | 0.30221 | 0.24182 | 0.24772 | 0.22522 | 0.19554 | 0.16807 | 0.12541 | 0.099782 | 0.12643 | 0.10732 | 0.11397 | 0.10004 | 0.031217 | 0.062805 | 0.074799
turve | 0.199 | 0.199 | 0.205 | 0.195 | 0.195 | 0.217 | 0.214 | 0.2117 | 0.2005 | 0.1875 | 0.18992 | 0.20717 | 0.2048 | 0.21523 | 0.20151 | 0.17684 | 0.20067 | 0.21882 | 0.19641 | 0.17208 | 0.19224 | 0.19408 | 0.16163 | 0.13869 | 0.14576 | 0.16219 | 0.14744 | 0.14538 | 0.15534 | 0.15334 | 0.14104 | 0.10581 | 0.10135 | 0.083527 | 0.058828
puu, muu bio | 0.022145 | 0.02156 | 0.023416 | 0.031934 | 0.042986 | 0.046541 | 0.055147 | 0.062894 | 0.066388 | 0.075 | 0.09802 | 0.092722 | 0.10453 | 0.10546 | 0.12635 | 0.15642 | 0.14392 | 0.13975 | 0.16322 | 0.1802 | 0.18143 | 0.22823 | 0.24684 | 0.28141 | 0.30562 | 0.32067 | 0.31155 | 0.32858 | 0.32844 | 0.34927 | 0.38551 | 0.42787 | 0.43596 | 0.46139 | 0.47428
Jäte | 0.016367 | 0.018049 | 0.019489 | 0.035125 | 0.051819 | 0.057849 | 0.065875 | 0.075626 | 0.072863 | 0.080138 | 0.091704 | 0.078059 | 0.084735 | 0.091183 | 0.095949
hukkalämmöt | 0.0037171 | 0.0091128 | 0.01022 | 0.016319 | 0.015942 | 0.02025 | 0.022542 | 0.023852 | 0.031236 | 0.033995 | 0.02203 | 0.03448 | 0.035861 | 0.037931 | 0.043306 | 0.054942 | 0.083124 | 0.094681 | 0.094361 | 0.108 | 0.13681 | 0.141 | 0.1351 | 0.19157 | 0.20578
muu | 0.021855 | 0.02144 | 0.019584 | 0.015066 | 0.012014 | 0.011459 | 0.012753 | 0.014306 | 0.025212 | 0.0243 | 0.014955 | 0.015253 | 0.016904 | 0.01415 | 0.011605 | 0.015578 | 0.017696 | 0.017405 | 0.027406 | 0.028922 | 0.009294 | 0.0096663 | 0.014884 | 0.010968 | 0.0055777 | 0.011187 | 0.0068207 | 0.005375 | 0.00604 | 0.0062109 | 0.0036086 | 0.002601 | 0.0025955 | 0.002271 | 0.0062946
dummy | 1
*Includes waste heat, heat pumps and electric boilers
Fossil fuels have increasingly been replaced by biomass and recovered heat.
Use of biomass has more than doubled since 2010.
Amount of heat recovery has nearly fivefold compared to 2010. Fuel consumption is avoided by making use of surplus heat.

## Slide 11: The use of excess heat and electricity remained on the same level with the previous year In 2024, the heat demand was lower than normal because the year was warmer than normal
Chart: GWh
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Hukkalämmöt | 730.7 | 777.5 | 986.5 | 1177.1 | 1123.2 | 1209.9 | 1283.9 | 1282.5 | 1405.9 | 2231.8 | 2970.2 | 3302.55 | 3373 | 3843.1 | 4530.65 | 5447.2002 | 4982.0799 | 6994.596 | 7042.2142
Fuel consumption can be avoided by making use of surplus heat. Heat can be recovered from data centers, industrial processes, flue gases, sewage water etc.
Electric boilers played a significant role in 2024 and they produced 1540 GWh heat

## Slide 12: Use of biomass made a slight downturn
Chart: GWh
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Kaukolämpö ja yhteistuotantosähkö | 3805.96 | 4046.42 | 4672.58 | 4986.32 | 5773.9 | 6950.92 | 6963.24 | 6744.98 | 7489.08 | 9130.04 | 11207.8 | 12148.74 | 14342.78 | 15819.54 | 17238.68 | 17013.64 | 18302.69 | 19605.7 | 19918.05 | 21053.47 | 20898.86 | 27208.3 | 26561.84 | 27119.74 | 26077.1436
In municipalities where district heating is provided
  85 per cent of networks heat comes from renewable fuels or recovered heat
Renewable fuels used in producing district heat are e.g. forest fuelwood, industrial wood residue, wood pellets, bio share of municipal waste.
Use of renewables in the production of district heat and cogeneration

## Slide 13: Future scenarios for district heating
Electrifying district heat production replaces fossil fuels and peat and reduces the need for energy use of biomass

## Slide 14: Electrifying district heat production replaces fossil fuels and peat and reduces the need for energy use of biomass
Source: Member survey in spring 2024
Chart: GWh
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Electric boilers | 0 | 60.1128 | 545.0053 | 1136.98 | 2714.9761 | 3674.1381 | 3367.0448 | 3189.1007 | 2916.8131 | 3049.5196
Waste heat and heat pumps | 4399.0751 | 4305.4355 | 5344.3811 | 5912.9244 | 7671.6485 | 9048.9057 | 9988.9999 | 10952.503 | 12085.6067 | 12557.3936

## Slide 15: Use of fossil fuels and peat is falling rapidly
Source: Member survey in spring 2024
Chart: GWh
| 2021 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Coal | 4732.6503 | 3555.1815 | 2068.9332 | 701.8362 | 60.5918 | 51.7532 | 38.5996 | 32.5598 | 32.4947
Gas | 4112.2727 | 2215.4203 | 2279.9049 | 1772.9447 | 1438.3532 | 1565.3035 | 1569.8088 | 1332.0834 | 382.3958
Oil | 977.8003 | 393.3198 | 363.5685 | 171.3395 | 138.7935 | 146.0969 | 100.4301 | 86.1585 | 75.5338
Peat | 2932.8742 | 2084.654 | 1590.7702 | 1078.5061 | 703.6558 | 480.9572 | 381.5879 | 256.5588 | 159.1675

## Slide 16: The share of biomass and waste in district heating will decrease slightly towards the end of the decade
Source: Member survey in spring 2024
Chart: GWh
| 2021 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Biomass | 12279.7688 | 14035.2066 | 14743.1868 | 14078.6987 | 13073.322 | 12553.9203 | 12044.0575 | 11559.6008 | 11994.9323
Municipality waste | 2525.9156 | 2919.2427 | 2918.3588 | 2788.5796 | 2751.5996 | 2733.2151 | 2605.5318 | 2542.1309 | 2483.7246
Recycled fuels | 597.6229 | 569.091 | 656.4224 | 727.5218 | 716.6498 | 657.8309 | 598.7791 | 604.825 | 609.1243

## Slide 17: Energy sources for district heat supply 1990-2030
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
hiili | 0.436 | 0.451 | 0.41 | 0.412 | 0.402 | 0.375 | 0.3763 | 0.3611 | 0.2946 | 0.2782 | 0.2644 | 0.27427 | 0.26223 | 0.26059 | 0.25055 | 0.236 | 0.25409 | 0.23995 | 0.21754 | 0.22213 | 0.20477 | 0.22702 | 0.22332 | 0.24115 | 0.22424 | 0.19569 | 0.22914 | 0.22892 | 0.1944 | 0.17641 | 0.11486 | 0.11481 | 0.152 | 0.080049 | 0.065969 | 0.022375 | 0.001936 | 0.0016568 | 0.0012382 | 0.0010466 | 0.0010469
öljy | 0.11 | 0.104 | 0.102 | 0.094 | 0.1 | 0.087 | 0.0824 | 0.0602 | 0.0709 | 0.0785 | 0.0841 | 0.091413 | 0.083644 | 0.080872 | 0.06411 | 0.057348 | 0.063641 | 0.065904 | 0.048745 | 0.072848 | 0.071663 | 0.046647 | 0.050259 | 0.0295 | 0.02814 | 0.029404 | 0.030642 | 0.021658 | 0.022122 | 0.019301 | 0.012498 | 0.029796 | 0.057 | 0.027202 | 0.011494 | 0.0054625 | 0.0044346 | 0.0046769 | 0.0032216 | 0.0027695 | 0.0024335
maakaasu | 0.211 | 0.203 | 0.24 | 0.252 | 0.248 | 0.263 | 0.2594 | 0.2898 | 0.3424 | 0.3565 | 0.34489 | 0.31005 | 0.31767 | 0.30738 | 0.32993 | 0.33756 | 0.29743 | 0.29432 | 0.31545 | 0.28982 | 0.30221 | 0.24182 | 0.24772 | 0.22522 | 0.19554 | 0.16807 | 0.12541 | 0.099782 | 0.12643 | 0.10732 | 0.11397 | 0.10004 | 0.031 | 0.062805 | 0.0724 | 0.056327 | 0.045957 | 0.050109 | 0.050357 | 0.042818 | 0.01232
turve | 0.199 | 0.199 | 0.205 | 0.195 | 0.195 | 0.217 | 0.214 | 0.2117 | 0.2005 | 0.1875 | 0.18992 | 0.20717 | 0.2048 | 0.21523 | 0.20151 | 0.17684 | 0.20067 | 0.21882 | 0.19641 | 0.17208 | 0.19224 | 0.19408 | 0.16163 | 0.13869 | 0.14576 | 0.16219 | 0.14744 | 0.14538 | 0.15534 | 0.15334 | 0.14104 | 0.10581 | 0.101 | 0.083527 | 0.050132 | 0.033892 | 0.022482 | 0.015397 | 0.012241 | 0.0082468 | 0.005128
puu, muu bio | 0.022145 | 0.02156 | 0.023416 | 0.031934 | 0.042986 | 0.046541 | 0.055147 | 0.062894 | 0.066388 | 0.075 | 0.09802 | 0.092722 | 0.10453 | 0.10546 | 0.12635 | 0.15642 | 0.14392 | 0.13975 | 0.16322 | 0.1802 | 0.18143 | 0.22823 | 0.24684 | 0.28141 | 0.30562 | 0.32067 | 0.31155 | 0.32858 | 0.32844 | 0.34927 | 0.38551 | 0.42787 | 0.436 | 0.46139 | 0.47428 | 0.44146 | 0.41731 | 0.40149 | 0.38596 | 0.37118 | 0.38606
Jäte | 0.016367 | 0.018049 | 0.019489 | 0.035125 | 0.051819 | 0.057849 | 0.065875 | 0.075626 | 0.072863 | 0.080138 | 0.091704 | 0.078059 | 0.085 | 0.091183 | 0.095949 | 0.088903 | 0.087916 | 0.087497 | 0.083581 | 0.081714 | 0.08002
hukkalämmöt | 0.0037171 | 0.0091128 | 0.01022 | 0.016319 | 0.015942 | 0.02025 | 0.022542 | 0.023852 | 0.031236 | 0.033995 | 0.020503 | 0.032805 | 0.031697 | 0.03348 | 0.037949 | 0.045369 | 0.082858 | 0.091731 | 0.091571 | 0.10574 | 0.13679 | 0.14062 | 0.134 | 0.17115 | 0.18755 | 0.2433 | 0.28115 | 0.3118 | 0.34337 | 0.38051 | 0.3966
sähkökattila | 0.0015265 | 0.001675 | 0.0041644 | 0.0044507 | 0.0053572 | 0.0095731 | 0.00026613 | 0.0029493 | 0.0027895 | 0.0022559 | 1.5597e-05 | 0.00038437 | 0.001 | 0.020422 | 0.036253 | 0.08508 | 0.11592 | 0.10631 | 0.10083 | 0.092281 | 0.096772
muu | 0.021855 | 0.02144 | 0.019584 | 0.015066 | 0.012014 | 0.011459 | 0.012753 | 0.014306 | 0.025212 | 0.0243 | 0.014955 | 0.015253 | 0.016904 | 0.01415 | 0.011605 | 0.015578 | 0.017696 | 0.017405 | 0.027406 | 0.028922 | 0.009294 | 0.0096663 | 0.014884 | 0.010968 | 0.0055777 | 0.011187 | 0.0068207 | 0.005375 | 0.00604 | 0.0062109 | 0.0036086 | 0.002601 | 0.003 | 0.002271 | 0.0062946 | 0.023194 | 0.022898 | 0.021059 | 0.019208 | 0.019441 | 0.019625
dummy | 1
Source for 2024-2030: Member survey in spring 2024
*includes heat pumps and heat recovery

## Slide 18: Carbon dioxide emissions from district heating are decreasing

## Slide 19: CO2-emissions from district heat production decreased by 19 %
CO2-emissions from district heat production in 2024 were 2,5 Million tons and decreased by 19 % from the previous year
Chart: Mill. t CO2
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
CO2-emissions, Mill. t CO2 | 6.6936 | 7.0385 | 5.946 | 5.7351 | 5.1483 | 5.6448 | 5.414 | 5.4496 | 4.9956 | 3.7555 | 4.0079 | 4.0404 | 3.1334 | 2.5384
District heat production, TWh | 34.0276 | 37.1357 | 34.9452 | 34.7437 | 33.2675 | 36.5511 | 36.5592 | 37.0768 | 36.5673 | 33.6354 | 39.0958 | 36.7578 | 36.7393 | 35.4821

## Slide 20: Specific CO2-emissions from district heat production have decreased by 65 % since 2010
Chart: g CO2 /kWh
| 1976 | 1980 | 1985 | 1987 | 1990 | 1995 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 276.1072 | 279.3688 | 292.2882 | 290.7152 | 271.6758 | 244.1654 | 229.7806 | 222.1 | 229.6 | 225 | 222.6 | 216.5 | 207.6 | 214.3 | 221.3 | 204.5 | 206.5 | 202.3 | 196.6 | 192.2 | 178.5 | 170.3 | 158.8 | 159.7 | 151.4 | 150.3 | 140.7 | 122.9 | 110.4 | 116 | 85.2862 | 71.5394
Source: Statistics Finland (2000...2022); Finnish Energy (1976...1999, 2023…2024)
  Specific emissions from district heat production in 2024 were 72 gCO2/kWh(*, which
    Decreased by 16 % from the previous year
    Decreased by 65 % since 2010
*) Fuels used in combined heat and power production were allocated according to the benefit allocation method

## Slide 21: The CO2-emissions from Finland’s energy production are decreasing
CO2-emissions of electricity and district heating production 4,6 million tons in year 2024
Emissions have declined 86 % compared to 2000s highest emission year 2003
Chart: million t CO2
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023* | 2024*
Condensing power | 6.6 | 9.7 | 11.2 | 18.6 | 15.3 | 5.2 | 15.2 | 12.8 | 7.5 | 7.7 | 11.9 | 8.1 | 4.3 | 7.1 | 5.3 | 3.2 | 3.7 | 2.9 | 3.9 | 2.3 | 1.9 | 2.6 | 2.3 | 1.2946 | 0.90203
CHP electricity and district heating | 10.6 | 12.3 | 12.5 | 12.9 | 12.5 | 11.7 | 12.1 | 12.2 | 11.4 | 11.7 | 12.6 | 11 | 10.5 | 10 | 9.4 | 8.8 | 9.3 | 9.2 | 9.2 | 8.6 | 6.3 | 6.3 | 5.7 | 3.1072 | 2.294
Separate production of district heating | 1.5 | 1.5 | 1.6 | 1.6 | 1.5 | 1.5 | 1.7 | 1.8 | 1.7 | 2.1 | 2.4 | 2.1 | 2.7 | 2 | 1.8 | 1.5 | 1.7 | 1.4 | 1.4 | 1.3 | 1.3 | 1.6 | 1.7 | 1.6333 | 1.3994

## Slide 22: District heat is the most common source of space heating in Finland

## Slide 23: Market share of space heating 2022 Residential, commercial and public buildings
Lähde: Statistics Finland
The electricity consumed by heat pumps has been estimated by Finnish Energy.
Heat pump: ambient energy extracted with heat pumps, and electricity consumption of heat pumps
Electricity: includes the electricity consumption of heat distribution equipment and electric sauna stoves
Wood: includes the wood used by sauna stoves
Chart: 
| District heat | Electricity | heat pump, electricity consumption | heat pump | wood | fuel oil | Other
 | 0.45028 | 0.16502 | 0.075193 | 0.13159 | 0.11764 | 0.05304 | 0.0072404

## Slide 24: The number of building permits applied for for residential construction has fallen strongly
Source: Statistics Finland
Chart: Million m3
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024M10
Small homes | 12.4007 | 12.0522 | 10.6825 | 8.1427 | 7.1363 | 9.0812 | 8.9435 | 7.8036 | 6.2437 | 5.5947 | 5.0089 | 5.3409 | 5.5304 | 5.3492 | 4.9647 | 5.0935 | 6.246 | 4.9647 | 2.8076 | 2.6091
Apartment buildings | 4.2529 | 4.2934 | 4.1381 | 3.6171 | 4.0092 | 5.2032 | 5.6295 | 5.399 | 4.3746 | 5.2827 | 6.1046 | 7.2666 | 9.0799 | 7.7929 | 7.0027 | 7.5375 | 8.0194 | 6.6227 | 4.1655 | 2.8828
Other residential buildings | 0.15339 | 0.26904 | 0.13832 | 0.23062 | 0.28494 | 0.27866 | 0.36425 | 0.46242 | 0.33535 | 0.46643 | 0.29301 | 0.3704 | 0.37967 | 0.18039 | 0.1312 | 0.06389 | 0.21856 | 0.25139 | 0.18029 | 0.24458
Commercial and office buildings | 6.6607 | 9.8862 | 12.1025 | 8.5499 | 8.4088 | 6.4567 | 6.8587 | 6.1524 | 6.5741 | 5.2343 | 5.7643 | 6.0218 | 7.1234 | 5.9048 | 6.1801 | 4.9393 | 4.9577 | 4.8046 | 4.123 | 4.8873
Public service buildings | 2.8448 | 2.3414 | 2.9261 | 3.2012 | 3.9677 | 3.3263 | 2.911 | 3.4845 | 3.5869 | 2.9648 | 4.1477 | 4.7353 | 4.3488 | 5.277 | 6.9709 | 5.7439 | 5.5805 | 4.7788 | 5.0393 | 3.307
Industrial and warehouse buildings | 12.0651 | 12.9456 | 16.5069 | 14.5971 | 9.0425 | 8.4163 | 12.3771 | 9.4427 | 8.8448 | 9.4185 | 10.658 | 10.8471 | 10.792 | 12.2302 | 13.2106 | 11.8633 | 15.1834 | 14.209 | 11.2894 | 11.3144
Agricultural buildings and shelters | 4.5562 | 5.3188 | 5.4794 | 5.4401 | 5.1806 | 4.5694 | 4.2613 | 3.682 | 5.2608 | 3.1195 | 2.8869 | 4.0351 | 3.3906 | 3.9315 | 4.451 | 3.4749 | 2.4262 | 1.5639 | 1.1683 | 1.7852
Other buildings | 5.1342 | 5.3798 | 5.5085 | 5.1593 | 4.4884 | 4.6519 | 4.5488 | 4.3467 | 3.8178 | 3.3803 | 3.0389 | 3.1948 | 2.8083 | 2.8741 | 2.7069 | 2.9126 | 3.3128 | 2.3833 | 1.7395 | 1.6114

## Slide 25: District heating is the most popular method of heating in new buildings
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Kaukolämpö | 0.449 | 0.444 | 0.447 | 0.436 | 0.481 | 0.48691 | 0.49727 | 0.49223 | 0.49129 | 0.48181 | 0.51336 | 0.51069 | 0.48132 | 0.48695 | 0.44623 | 0.44998 | 0.52651 | 0.56247 | 0.52843 | 0.57088 | 0.5133 | 0.57272 | 0.54415 | 0.5095 | 0.5775 | 0.62258 | 0.63253 | 0.64412 | 0.57601 | 0.57889 | 0.5104 | 0.51376 | 0.46154 | 0.51222 | 0.43384
Sähkö | 0.315 | 0.312 | 0.307 | 0.312 | 0.275 | 0.24801 | 0.21456 | 0.22823 | 0.2444 | 0.26233 | 0.2484 | 0.26006 | 0.2852 | 0.258 | 0.27692 | 0.29848 | 0.25056 | 0.22045 | 0.19544 | 0.18796 | 0.22844 | 0.17866 | 0.17599 | 0.16906 | 0.13384 | 0.13648 | 0.11955 | 0.12082 | 0.14412 | 0.12421 | 0.15158 | 0.14131 | 0.10276 | 0.089281 | 0.11295
Lämpöpumppu | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.007994 | 0.010341 | 0.014757 | 0.018112 | 0.024206 | 0.037017 | 0.040396 | 0.04284 | 0.047442 | 0.05424 | 0.072395 | 0.065787 | 0.13232 | 0.15215 | 0.19121 | 0.20847 | 0.2012 | 0.17306 | 0.16929 | 0.1788 | 0.19798 | 0.21312 | 0.2442 | 0.27762 | 0.36099 | 0.3372 | 0.34494
Puu | 0.049 | 0.064 | 0.074 | 0.106 | 0.109 | 0.11352 | 0.099025 | 0.092166 | 0.070935 | 0.059078 | 0.058067 | 0.061882 | 0.063524 | 0.065246 | 0.068209 | 0.071804 | 0.07126 | 0.054738 | 0.059524 | 0.057248 | 0.058361 | 0.047459 | 0.054923 | 0.055246 | 0.046247 | 0.029852 | 0.033381 | 0.019943 | 0.02953 | 0.034259 | 0.03136 | 0.022535 | 0.017838 | 0.024276 | 0.023467
Öljy ja kaasu | 0.12 | 0.138 | 0.137 | 0.123 | 0.101 | 0.11553 | 0.11672 | 0.13529 | 0.15979 | 0.16379 | 0.13001 | 0.13163 | 0.11929 | 0.13152 | 0.13469 | 0.1101 | 0.071147 | 0.082157 | 0.10253 | 0.053809 | 0.046536 | 0.03098 | 0.018289 | 0.032128 | 0.018016 | 0.014495 | 0.027158 | 0.01346 | 0.023299 | 0.0156 | 0.012806 | 0.0061082 | 0.0075569 | 0.0071136 | 0.0036547
Source: Statistics Finland, Granted building permits (heated cubic volume)

## Slide 26: Main heating methods in new buildings
Chart: 
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | Apartment buildings | Other buildings | Small homes
District heating | 6816899 | 8411211 | 7127974 | 6315022 | 6571760 | 6451413 | 4802176 | 3112742 | 1592846 | 10259704 | 9966040 | 8704115 | 10449024 | 7913786 | 9351937 | 8361968 | 7788969 | 4745344 | 1177749 | 1168262 | 1060300 | 891808 | 765460 | 858261 | 704973 | 303825 | 210996
Heat pumps | 229766 | 265694 | 421487 | 421202 | 818241 | 1290286 | 1617891 | 856088 | 355499 | 2106727 | 2523036 | 2892551 | 3662961 | 3971832 | 4678519 | 6756927 | 4981496 | 3737980 | 2549091 | 2636936 | 2491898 | 2415986 | 2506714 | 3034514 | 2472686 | 1539133 | 1113659
Others | 18014 | 64377 | 49244 | 20624 | 15183 | 62640 | 59816 | 20382 | 34900 | 4500902 | 3960482 | 5095328 | 4956419 | 5814673 | 4662544 | 3722078 | 2498594 | 2748574 | 1202526 | 1348808 | 1483707 | 1366267 | 1503078 | 2040321 | 1552643 | 775141 | 556130
Source: Statistics Finland, Granted building permits (heated cubic volume)

## Slide 27: District cooling is cost-effective and environmentally friendly

## Slide 28: The use of district cooling increased by 20 % in 2024 The warm year increased the need for cooling
District cooling sales increased by 20 % from the previous year
Connected load increased by 3 %
Energy companies which sold district cooling 2024:
Etelä-Savon Energia Oy
Fortum Power and Heat Oy
Helen Oy
Jyväskylän Energia Oy
Kuopion Energia Oy
Lahti Energia Oy
Lempäälän Lämpö Oy
Loimua Oy, Hämeenlinna
Oulun Energia Oy
Pori Energia Oy
Tampereen Sähkölaitos Oy
Turku Energia Oy
Vierumäen Infra Oy
Chart: Sales MWh
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
delivered energy | 4414 | 8710 | 13455 | 15732 | 25989 | 46560 | 55682 | 60020 | 79051 | 110207 | 125881 | 130953 | 169217 | 190999 | 181588.209 | 204921.1 | 222575 | 300648 | 280980.2 | 288107.64 | 336293.624 | 333468.7379 | 328313.076 | 400900.966
connected load | 6.3 | 15.1 | 20.1 | 28.5 | 41.2 | 67.5 | 73.6 | 101.3 | 116.9 | 134.2 | 155.9 | 183 | 204.2 | 225.754 | 243.374 | 276.3 | 297.8 | 324.5 | 372.11 | 411.961 | 446.06 | 465.23 | 491.412 | 513.412

## Slide 29: District cooling is produced efficiently
Same heat pumps often produce both heat and cooling energy
  the cooling water is cooled and the district heating water is warmed up in the same process.
District cooling also utilizes the ambient energy from sea, lakes and rivers as well as outdoor air whenever the temperature is low enough.
Chart: 
| Compression chilling | Absorption chilling | Heat pump | Free cooling
Tuotantomuodot | 0.08 | 0.67 | 0.25